## Slide 1: Design of the gas cell for IGLIS experiments
Evgeny Mogilevskiy, IKS Leuven

## Slide 2: Outlook
Introduction
Experimental setup
Model
Comparison experiment/simulation
New design
Validation
Conclusions

## Slide 3: Schematic of the Heavy Element Laser IOnization Spectroscopy project
How to carry atoms through the cell?
Where are they lost?
How to improve transport efficiency?
Hydrodynamic simulation is needed
IGLIS – In Gas Laser Ionization Spectroscopy

## Slide 4: Leuven Isotope Separator On-Line (LISOL) Dual-chamber gas cell
Beam line
Gas supply
Laser beam
Gas: Ar or He
Pressure up to 500 mbar
Room temperature
Exit hole: 0.5 or 1 mm diameter
Flowrate: ~102 cm3/s

## Slide 5: Leuven Isotope Separator On-Line (LISOL)
Cyclotron beam
Gas Cell
SPIG
Extraction electrode
Gas from purifier
Laser beams

## Slide 6: Physics in the cell
Gas flow: laminar or turbulent
  Laminar:
    Streamlines are smooth and do not intersect each other
    Could exist is viscosity is big enough
  Turbulent
    Appears due to instability of a laminar flow
    Contains a lot of small vortices
    Chaotically time-dependent
Atoms-walls interaction
  If an atom reaches the wall it sediments on it:
Transport of atoms
  Convection: with a gas along the streamlines
  Diffusion: over the gas flow, across the streamlines, pressure-dependent
  Turbulent diffusion: with turbulent vortices, very strong

## Slide 7: Flow in the cell
Exit hole 0.5 mm
Pressure 500 mbar

## Slide 8: Concentration field in cell
Region where atoms are produced must be stated
Transport efficiency: eff=influx/outflux
log(c)

## Slide 9: Experiment
58Ni beam 3e9 pps 185 MeV.
Two Mo windows 4.15 um
Pressure from 480 mbar to 150 mbar
Measurements:
Ion signal for a single laser pulse (cyclotron in DC mode)
Ion signal for high repetition laser (cyclotron 50 ns ON 1500 ms OFF)
Relative efficiencies for different pressures
Yu. Kudryavtsev et al (2009) NIM

## Slide 10: Stopping area
SRIM calculation

## Slide 11: Single laser pulse
First peak for atoms near the exit hole
Second maximum for atoms from high concentration area
Chart: Time, ms

## Slide 12: Simulation (p=300 mbar)

## Slide 13: High repetition laser
Chart: 300 mbar
Chart: 400 mbar
Chart: Relative efficiency
| 400 | 300 | 200
Calculation | 0.82423 | 0.47955 | 0.1247
Experiment | 0.92 | 0.57 | 0.11
Maximal abs. efficiency 23% for 480 mbar

## Slide 14: Conclusions from comparison
Most features of output signal are simulated
The model presented can be used for a new designs
There is a laminar flow in the cell
Majority of the losses can be explained by diffusion
Sharp edges and turnings should be avoided
Losses structure

## Slide 15: Horn cell
inlet
plenum
obstacle
Anti-vortex grid
Beam window
Filament windows
Laser windows
Laser windows
Ion collector
Exit hole
The flow is much more uniform
Exit hole 1 mm
Pressure 500 mbar

## Slide 16: Horn cell diffusion
Chart: Losses D=3.8
| -5 | -2.5 | 0 | 2.5 | 5
cell | 0.07121 | 0.029002 | 0.024331 | 0.059608 | 0.14194
turning | 0.17075 | 0.13874 | 0.11722 | 0.11282 | 0.11743
ic | 0.061397 | 0.057252 | 0.049829 | 0.041832 | 0.034365
contr | 0.076487 | 0.074967 | 0.068276 | 0.058496 | 0.047697
laser | 0.01638 | 0.016538 | 0.015511 | 0.013602 | 0.011233
out | 0.040405 | 0.041399 | 0.039476 | 0.035199 | 0.029483
Chart: Losses D=7.6
| -5 | -2.5 | 0 | 2.5 | 5
cell | 0.21565 | 0.15838 | 0.15166 | 0.19669 | 0.29156
turning | 0.27522 | 0.2799 | 0.26973 | 0.24824 | 0.21665
ic | 0.077841 | 0.083252 | 0.083097 | 0.077522 | 0.067141
contr | 0.072753 | 0.078956 | 0.079907 | 0.075352 | 0.065808
laser | 0.019631 | 0.021499 | 0.021962 | 0.020893 | 0.018375
out | 0.022525 | 0.024751 | 0.025373 | 0.024216 | 0.021355
Chart: Losses D=1.9
| -5 | -2.5 | 0 | 2.5 | 5
cell | 0.010442 | 0 | 0 | 0 | 0.044431
turning | 0.074344 | 0.034936 | 0.021049 | 0.032584 | 0.064161
ic | 0.038038 | 0.024001 | 0.014269 | 0.011351 | 0.013341
contr | 0.047577 | 0.034299 | 0.022483 | 0.016095 | 0.0147
laser | 0.013356 | 0.010276 | 0.0071227 | 0.0050559 | 0.0042127
out | 0.046365 | 0.036805 | 0.026252 | 0.018675 | 0.014959
Chart: Efficiency
| -5 | -2.5 | 0 | 2.5 | 5
D=1.9 | 0.76988 | 0.86201 | 0.91235 | 0.91048 | 0.84419
D=3.8 | 0.56338 | 0.6421 | 0.68536 | 0.67844 | 0.61785
D=7.6 | 0.31638 | 0.35326 | 0.36827 | 0.35709 | 0.31911

## Slide 17: Validation by a simple model
Assumptions:
  Axisymmetric geometry: narrowing instead of turning, no windows
  No viscous effects: uniform velocity field, its magnitude inversely proportional to area
  No streamline diffusion (terms about 0.04 are omitted)
Variable transformation
  Problem is equivalent to a diffusion problem in a straight tube

## Slide 18: Simple model

## Slide 19: Conclusions
Diffusion is responsible for losses inside the gas cell
In order to reduce it the flow should be laminar and smooth
There is a certain minimal level of unavoidable diffusive losses
The horn cell provides rate of diffusive losses which are very close to the minimal ones
Change of the cell improves the transport efficiency by factor of 3.

## Slide 20
Thank you for your attention

## Slide 21: Single laser pulse
Chart: c(z)
| 12 | 14 | 16 | 18 | 20 | 22 | 25 | 28 | 31 | 34 | 35.5 | 37 | 38.5 | 40 | 41.5 | 43
c_in | 0.00444 | 0.01304 | 0.0213 | 0.02095 | 0.01541 | 0.00957 | 0.005 | 0.003988 | 0.004075 | 0.004415 | 0.0044275 | 0.00478 | 0.00493 | 0.00508 | 0.005305 | 0.00533
Chart: f(z,t)
Chart: e(z)
| 12 | 14 | 16 | 18 | 20 | 22 | 25 | 28 | 31 | 34 | 35.5 | 38.5 | 40 | 43
 | 0.010068 | 0.010068 | 0.010068 | 0.31337 | 0.55539 | 0.68007 | 0.80007 | 0.8452 | 0.87661 | 0.8905 | 0.89834 | 0.90683 | 0.91532 | 0.96625
Output signal

## Slide 22: High repetition laser pulses
Chart: Time, ms
Pressure | Start of the signal (calculated) | Maximum of the signal position (calculated)
480 mbar | 150 ms (240 ms) | 305 ms (650 ms)
400 mbar | 170 ms | 460 ms
300 mbar | 250 ms | 560 ms
200 mbar | 300 ms | 740 ms
Cyclotron:
50 ms ON
1500 ms OFF
Laser repetition 100Hz

## Slide 23: What is wrong?
Diffusion coefficient?
  Not affect time
Heat transfer is the cell?
  Not sufficient at all
Stopping area location?
  Depends on window thickness known with 20% tolerance
Chart: window thickness, um
| 4 | 4.5 | 5 | 5.5
 | 32 | 24.5 | 17.5 | 9.5

## Slide 24: Evacuation time (p=480 mbar)
Position of maximum – weighted average of the function
In experiment tmax=305 ms => Stopping distance <20mm.
Assume stopping distance to be 19 mm.
20 mm from window
-6
-4
-2
0
2
4
6
-10
-8
-6
-4
-2
0
2
4
280
320
360
400
440
480
520
560
600
640
18 mm from window